Monster 821 Technical specification

Engine

Type			Testastretta 11° L-Twin, 4 Desmodromically actuated valves per cylinder,

liquid cooled

Displacement		821 cc

Bore x Stroke		88 x 67.5 mm

Compression ratio	12.8:1

Power			82.4 kW (112 hp) @ 9,250 rpm

Torque			89.4 Nm (65.8 lb-ft) @ 7,750 rpm

Technical data referring to power and torque was measured on an engine

test stand at Ducati.

Fuel injection		Electronic fuel injection system, 53mm throttle bodies with full Ride by Wire

Exhaust		Stainless steel muffler and aluminium and cap; lightweight 2-1 system with

catalytic converter with 2 lambda probes

Transmission

Gearbox		6 speed

Primary drive		Straight cut gears, ratio 1.85:1

Ratio			1=37/15 2=30/17 3=28/20 4=26/22 5=24/23 6=23/24

Final drive		Front sprocket 15; Rear sprocket 46

Clutch			APTC slipper and self-servo wet multiplate clutch with control cable

Chassis

Frame			Tubular steel Trellis frame attached to the cylinders head

Front suspension	Upside down 43 mm forks

Front wheel		10-spoke in light alloy 3.50" x 17"

Front Tyre		120/70 ZR 17 Pirelli Diablo Rosso II

Rear suspension	Progressive linkage with adjustable monoshock. Aluminium double-sided

swingarm

Rear wheel		10-spoke in light alloy 5.50" x 17"

Rear tyre		180/60 ZR17 Pirelli Diablo Rosso II

Front wheel travel	130 mm (5.1in)

Rear wheel travel	140 mm (5.5 in)

Front brake		2 x 320mm semi-floating discs, radially mounted Monobloc Brembo M4-32

callipers, 4-pistons, axiial pump with ABS as standard

Rear brake		245mm disc, 2-piston floating calliper with ABS as standard equipment

Instrumentation	LCD display

Dimensions and weight

Dry weight		179.5kg (395.7lb)

Weight data refers to the dry weight of the motorcycle without battery,

lubricants and coolants for liquid-cooled models.

Wet weight (KERB)	205.5 kg (453lb)

Kerb weights indicate total bike weight with all operating consumable liquids and a fuel tank filled to 90% of capacity (as per EC standard 93/93).

Seat height		Adjustable 785 - 810 mm (30.9 - 31.9 in)

Wheelbase		1480 mm (58.3 in)

Rake			24,3°

Trail			93.2 mm (3.7 in)

Fuel tank capacity	17.5l - (4.6 US gal)

Number of seats	Dual seat

Equipments

Standard Equipment	Riding modes,Power modes, DSP Ducati Safety Pack (ABS + DTC), RbW,

seat cover passanger handles, ready for anti-theft system and DDA

Warranty

Warranty		24 months unlimited mileage

Maintenance		15,000 km (9,000 m)/12 Months

service intervals

Valve clearance	30,000 km (18,000 m)

check

Emissions and Consumption

Standard		Euro 3