New Product

Hypermotard 939 : Get Hyped

ด้วยแรงบันดาลใจจากรถเดิร์ทไบค์แบบดั้งเดิม ประกอบกับดีไซน์ด้านข้างที่ดูเพรียวรับกับท้ายรถที่ยกสูง จนกลายเป็นเอกลักษณ์เฉพาะของ Hypermotard ที่ให้คุณสนุกแบบไร้ขีดจำกัดได้ทุกวัน แต่ยังคงความปลอดภัยได้ในทุกเส้นทาง ทั้งการเดินทางอันน่าตื่นเต้น หรือการขับขี่ในเมือง ด้วยเครื่องยนต์เทสตราสเทรทต้า อีเลฟเว่นดีกรีรุ่นใหม่ มาพร้อมออยคูลเลอร์ ให้กำลังได้ถึง 113 แรงม้า มาพร้อมเทคโนโลยีล้ำสมัย ทั้ง Riding Mode, ดูคาติ เซฟตี้ แพ็ค และแทร็คชั่นคอนโทรล รวมถึงระบบเบรก ABS

Technical Specification

Engine

Type			New Testastretta 11°, L-Twin cylinder, 4 valve per cylinder, Desmodromic,

liquid cooled

Displacement		937 cc

Bore x Stroke		94 x 67,5 mm

Compression ratio	13,1:1

Power			83.1 kW (113 hp) @ 9000 rpm

Torque			97.9 Nm (72.2 lb-ft) @ 7500 rpm

Technical data referring to power and torque was measured on an engine test

stand at Ducati.

Fuel injection		Magneti Marelli electronic fuel injection system. Throttle bodies with full Ride by

Wire system

Exhaust		Single stainless steel muffler with catalytic converter and two lambda probes.

Transmission

Gear box		6 speed

Primary drive		Straight cut gears, Ratio 1.85:1

Ratio			1=37/15 2=30/17 3=28/20 4=26/22 5=24/23 6=23/24

Final drive		Chain, Front sprocket 15, Rear sprocket 43

Clutch			Wet multiplate clutch mechanically operated, self-servo action on drive, slipper

action on over-run

Chassis

Frame			Tubular steel Trellis frame

Front suspension	43mm usd forks

Front wheel		10-spoke in light alloy 3.50" x 17"

Front Tyre		Pirelli Diablo Rosso II, 120/70 ZR17

Rear suspension	Progressive linkage with adjustable spring preload and rebound damping Sachs

monoshock. Aluminium single-sided swingarm

Rear wheel		10-spoke in light alloy 5.50" x 17"

Rear tyre		Pirelli Diablo Rosso II, 180/55 ZR17

Front wheel travel	170 mm (6.7 in)

Rear wheel travel	150 mm (5.9 in)

Front brake		2 x 320 mm semi-floating discs, radially mounted Brembo monobloc callipers,

4-piston 2-pad, axial pump with adjustable lever, with Bosch ABS as standard

Rear brake		245 mm disc, 2-piston calliper, with Bosch ABS as standard

Instrumentation		LCD display with Dot Matrix area

Dimensions and weight

Dry weight		181 kg (399 lb)

Weight data refers to the dry weight of the motorcycle without battery, lubricants

and coolants for liquid-cooled models.

Wet weight (KERB)	204 kg (450 lb)

Kerb weights indicate total bike weight with all operating consumable liquids and

a fuel tank filled to 90% of capacity (as per EC standard 93/93).

Seat height		870mm (34.2in)

Wheelbase		1.493 mm (58.8 in)

Rake			25,5°

Trail			104mm (4.1In)

Fuel tank capacity	16l - 4.2gallon (US)

Number of seats	Dual seat

Equipments

Standard Equipment	Riding Modes, Power Modes, Ducati Safety Pack (ABS + DTC), RbW. Ready for

anti-theft system, heated grips, sat-nav.

Warranty

Warranty		24 months unlimited mileage

Maintenance 		15,000 km (9,000 mi)/12 months

service intervals

Valve clearance check	30,000 km (18,000 mi)

Emissions and Consumption

Standard		Euro 4

Consumption		5,2 l/100 km - CO2 = 123 g/km